## Slide 1: Hard Real-Time Systems and Many-Core Platforms Alan Burns Real-Time Systems Group Department of Computer Science University of York United Kingdom

## Slide 2: Motivation
Temporal predictability is getting increasing difficult with multi- and many-core platforms
Advice to ‘use only one core’ in avionics white papers
How to bound interference across the hardware platform?

## Slide 3: Temporal Requirements
General task/thread model
Mixed criticality sporadic tasks
  Released by events or the passage of time
  Given any interval of time t the maximum number of releases of each task within t is known
Tasks synchronise and communicate as required
  i.e. not constrained
It follows that a time-triggered static schedule is not the solution

## Slide 4: Outline
Allocation
Networks-on-Chip
  Wormhole networks
Real-Time Analysis
  A tale of mistakes, corrections, errors and plagiarism
Predictability as an emergent property

## Slide 5: Allocation
Most theoretical results assume homogeneous architectures
Some work on
  Two processor types, e.g. big and small
  Variable speed processors
FPGAs, GPUs
More general heterogeneous models beginning to appear in literature

## Slide 6: Dynamic Allocation/Partitioning
Dhall effect, from 1978
For single processor systems EDF or DMPA for fixed priority scheduling are optimal
BUT
  50 tasks needing 2ms every 100
  1 task requires 100 in 101
  EDF and DMPA leads to unschedulable on 50 cores
  Clearly schedulable on 2 cores

## Slide 7: Dynamic Allocation/Partitioning
Later theoretical results indicate benefits from global (dynamic) task scheduling
But
  These results ignore overheads (migration costs)
  They make modelling of inter-task communication more problematic
Hence Partitioned task allocation is main focus of more practical research
Semi-partitioned gets most of the benefits
  C=D scheme, moves just one task per core

## Slide 8: Communication
Bus-based architectures are problematic
  In effect unbounded interference
Need a resource that can be scheduled (managed)
Hence Networks

## Slide 9: Networks – key characteristics
topology
  mesh, star, torus…
routing protocol
  deterministic, adaptive…
arbitration
  round-robin, priority preemptive, priority non-preemptive, TDM…
buffering
  FIFO, SAFC, SAMQ, DAMQ, hot potato…
flow control protocol
  handshake, credit-based…
switching protocol
  store-and-forward, circuit, wormhole

## Slide 10: Networks – key characteristics
topology
  mesh, star, torus…
routing protocol
  deterministic, adaptive…
arbitration
  round-robin, priority preemptive, priority non-preemptive, TDM…
buffering
  FIFO, SAFC, SAMQ, DAMQ, hot potato…
flow control protocol
  handshake, credit-based…
switching protocol
  store-and-forward, circuit, wormhole

## Slide 11: Wormhole switching
Packet is routed and forwarded as soon the header flit has arrived
  payload flits follow header
Input ports does not need to buffer a complete packet
  flits of a packet can be stored across multiple routers
Trade-off between buffer overheads and network contention

## Slide 12: Wormhole Switching
Switch
Switch
Switch
Switch
Switch
Switch
Terminal
Packet Header
Packet Data

## Slide 13: Wormhole Switching
Switch
Switch
Switch
Switch
Switch
Switch
Terminal
Packet Header
Packet Data

## Slide 14: Wormhole Switching
Switch
Switch
Switch
Switch
Switch
Switch
Terminal
Packet Header
Packet Data

## Slide 15: Wormhole Switching
Switch
Switch
Switch
Switch
Switch
Switch
Terminal
Packet Header
Packet Data

## Slide 16: Wormhole Switching
Switch
Switch
Switch
Switch
Switch
Switch
Terminal
Packet Header
Packet Data

## Slide 17: Wormhole Switching
Switch
Switch
Switch
Switch
Switch
Switch
Terminal
Packet Header
Packet Data

## Slide 18: Wormhole Switching
Switch
Switch
Switch
Switch
Switch
Switch
Terminal
Packet Header
Packet Data

## Slide 19: Wormhole Networks-on-Chip
Small buffering overheads of wormhole networks is particularly attractive to a special class of resource-constrained networks: Networks-on-Chip (NoCs)
  small buffers mean smaller area and lower energy dissipation
PE
PE
PE
PE
PE
PE
PE
PE
R
PE
R
R
R
R
R
R
R
R

## Slide 20: Wormhole Networks-on-Chip
PE
PE
PE
PE
PE
PE
PE
PE
R
PE
R
R
R
R
R
R
R
R
Core
Router
Link

## Slide 21: Wormhole Networks-on-Chip
PE
PE
PE
PE
PE
PE
PE
PE
R
PE
R
R
R
R
R
R
R
R
Link

## Slide 22
arbitration
routing
&
transmission
control
routing
&
transmission
control
data out
data in
data out
data in
data out
data in
data out
data in
data out
data in
PE
PE
PE
PE
PE
PE
PE
PE
R
PE
R
R
R
R
R
R
R
R
Wormhole Networks-on-Chip

## Slide 23: Wormhole Networks-on-Chip

## Slide 24: NoC parallelism and scalability
Multiple connections simultaneously
Notes: 24

## Slide 25: NoC performance
link contention leads to latency variability
task contention leads to latency variability
Notes: 25

## Slide 26: Task Scheduling
Priority Based scheduling
  Each task has a priority derived from its temporal characteristics
  Required WCET for each task
  Response-Time analysis enables the worst-case completion time (R) to be calculated
  This can then be compared with task deadline to ensure R <= D

## Slide 27: Priority preemptive virtual channels
Wormhole NoCs using virtual channels with priority preemptive arbitration can discriminate packets of different levels of urgency

## Slide 28: Priority preemptive virtual channels
…
highest priority
with remaining credit
data_in
credit_out
data_out
credit_in
…
routing
&
transmission
control
priority ID
…
highest priority
with remaining credit
…
routing
&
transmission
control
PE
PE
PE
PE
PE
PE
PE
PE
R
PE
R
R
R
R
R
R
R
R

## Slide 29: NoC Performance Evaluation
Many approaches to evaluate NoC performance
  full system prototyping
    cores + NoC in FPGA, running OS + application
    extremely costly setup time, can only explore few design alternatives
  accurate system simulation
    cycle-accurate model of cores + NoC, running OS + application
    extremely long simulation time, can only explore few design alternatives
  approximately-timed system simulation
    approximately-timed model of cores + NoC, executing an abstract model of the OS + application
  analytical system performance models
    worst-case latency estimation for restricted application characteristics

## Slide 30: Real-Time Analysis
A packet flow ti is a potentially unbounded sequence of packets, characterised by
  priority Pi
  period Ti - smallest inter-arrival interval
  no-load latency Ci – deterministic, function of # flits, # hops, router latency and link latency
  release jitter JRi
  deadline Di
Analysis aims to calculate worst case response time Ri for every ti, and check if Ri ≤ Di

## Slide 31: Real-Time Analysis
First approaches to analyse priority-preemptive wormhole networks came during the 90s
  Mutka (Workshop Parallel Distr Real-Time Sys 1994)
  Hary and Ozguner (IEE Proc CDT 1997)
Key idea is to consider the entire path of a packet as a single shared resource
  worst-case latency bound of a packet flow can be found by analysing the higher priority packet flows that share at least one link of its route
  assumes that interference from higher priority flows will be bounded by the number of “hits”, and each hit bounded by the no-load latency of the interfering flow

## Slide 32: Real-Time Analysis
PE
PE
PE
PE
PE
PE
PE
PE
R
PE
R
R
R
R
R
R
R
R
t4
t3
t2
t1
P1 > P2 > P3 > P4
t2
t4
t3
t1
  interference graph

## Slide 33: Real-Time Analysis
Kim et al (Conf Parallel Proc 1998) recognised that upstream indirect interference can also affect latency upper bounds
Shi&Burns (NOCS 2008) produced a response time formulation that conservatively models upstream indirect interference
PE
PE
PE
PE
PE
PE
PE
PE
R
PE
R
R
R
R
R
R
R
R
t2
t3
t1
P1 > P2 > P3

## Slide 34: Real-Time Analysis
Several lines of work were derived from Shi and Burns 2008
  well cited: 158 (Google Scholar)
  many works on priority assignment and task mapping
  a few on analysis improvement, aiming to make it tighter
    Nikolic et al (arxiv 2016) considered that the interference should not be calculated based on the full path, but the contention domain
    Kashif et al (IEEE Trans Comp 2015) attempted to analyse packet paths on a link-by-link manner, but assumed infinite buffering (i.e. did not consider backpressure)
    Kashif and Patel (RTAS 2016) attempted to consider buffering and backpressure effects
    all of them upper-bounded by Shi and Burns 2008

## Slide 35: Real-Time Analysis
  Xiong et al (GLSVLSI 2016) made two key contributions
  new formulation to the downstream indirect interference problem, aiming to capture a previously unseen issue: multi-point blocking
    showed that Shi and Burns 2008 is optimistic and unsafe (and so are all the analyses upper-bounded by it)
  new formulation to the upstream indirect interference problem, aiming to be tighter than Shi and Burns 2008
    was shown to be flawed by Indrusiak et al (arxiv 2016)

## Slide 36: Real-Time Analysis
Xiong et al published a corrected analysis in IEEE Trans Comp in 2017
  including the fix from Indrusiak at al (arxiv 2016) for the upstream indirect interference
  accounting downstream indirect interference as if it is direct interference, making worst-case response times safe even under multi-point blocking scenarios

## Slide 37: Newer Analysis – DATE 2018 (Best Paper)
Aims to reduce the pessimism when accounting for downstream indirect interference
Key ideas
  buffered interference: multi-point blocking is only caused by flits buffered over the routers shared between the flow under analysis and the flow causing interference
  buffered interference will reoccur for every downstream indirect interference hit suffered by the flow causing interference

## Slide 38: Proposed Analysis
Key ideas
  buffered interference: multi-point blocking is only caused by flits buffered over the routers shared between the flow under analysis and the flow causing interference
  upper-bounding buffer interference biij caused by tj on ti:
buffer spaces per router
link latency
number of hops shared between ti and tj

## Slide 39: Proposed Analysis
Key ideas
  buffered interference will reoccur for every downstream indirect interference hit suffered by the flow causing interference
  upper-bounding number of downstream indirect interference hits
for every flow that can cause downstream indirect interference on ti via tj
maximum number of hits that tj can suffer, causing buffered interference to be replenished

## Slide 40: Proposed Analysis
Caveat
  there are cases when the amount of downstream indirect interference is not enough to fill up the buffers up to the maximum possible amount of buffered interference
  in that case, revert to Xiong et al 2017 and consider downstream indirect interference instead

## Slide 41: Evaluation
Large-scale evaluation using synthetic scenarios
  4x4 and 8x8 NoCs
  each experiment has 100 randomly generated scenarios with N packet flows
    packet flows have periods between 0.5s and 0.5ms, packet length between 128 and 4096 flits, rate-monotonic priority and random source and destination PEs
  multiple experiments were performed by increasing N and checking how many of the 100 scenarios are fully schedulable, i.e. all its flows have R ≤ D
    for each analysis: Xiong et al (XLWX), Shi&Burns (SB), proposed (IBN)

## Slide 42: Evaluation – 4x4
Chart: 
| 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0 | 110.0 | 120.0 | 130.0 | 140.0 | 150.0 | 160.0 | 170.0 | 180.0 | 190.0 | 200.0 | 210.0 | 220.0 | 230.0 | 240.0 | 250.0 | 260.0 | 270.0 | 280.0 | 290.0 | 300.0 | 310.0 | 320.0 | 330.0 | 340.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 400.0 | 410.0 | 420.0 | 430.0
SB | 100 | 100 | 100 | 100 | 100 | 99 | 100 | 100 | 100 | 98 | 98 | 95 | 96 | 97 | 94 | 95 | 93 | 91 | 88 | 82 | 87 | 84 | 83 | 85 | 78 | 73 | 71 | 76 | 74 | 60 | 63 | 64 | 63 | 58 | 59 | 58 | 52 | 50 | 54 | 46
XLWX | 100 | 100 | 99 | 98 | 91 | 93 | 84 | 85 | 80 | 64 | 58 | 54 | 56 | 45 | 23 | 13 | 13 | 9 | 6 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
IBN2 | 100 | 100 | 100 | 99 | 98 | 98 | 99 | 96 | 94 | 90 | 87 | 82 | 88 | 78 | 67 | 71 | 63 | 55 | 49 | 43 | 51 | 43 | 36 | 33 | 25 | 24 | 9 | 13 | 10 | 3 | 8 | 5 | 0 | 4 | 2 | 1 | 0 | 2 | 1 | 0
IBN100 | 100 | 100 | 100 | 99 | 97 | 98 | 99 | 96 | 94 | 89 | 85 | 80 | 86 | 73 | 65 | 67 | 56 | 52 | 46 | 42 | 48 | 38 | 36 | 25 | 20 | 22 | 8 | 12 | 8 | 3 | 8 | 4 | 0 | 4 | 2 | 1 | 0 | 1 | 1 | 0
Chart: # flows per flow set
| 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0 | 110.0 | 120.0 | 130.0 | 140.0 | 150.0 | 160.0 | 170.0 | 180.0 | 190.0 | 200.0 | 210.0 | 220.0 | 230.0 | 240.0 | 250.0 | 260.0 | 270.0 | 280.0 | 290.0 | 300.0 | 310.0 | 320.0 | 330.0 | 340.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 400.0 | 410.0 | 420.0 | 430.0
SB | 100 | 100 | 100 | 100 | 100 | 99 | 100 | 100 | 100 | 98 | 98 | 95 | 96 | 97 | 94 | 95 | 93 | 91 | 88 | 82 | 87 | 84 | 83 | 85 | 78 | 73 | 71 | 76 | 74 | 60 | 63 | 64 | 63 | 58 | 59 | 58 | 52 | 50 | 54 | 46
XLWX | 100 | 100 | 99 | 98 | 91 | 93 | 84 | 85 | 80 | 64 | 58 | 54 | 56 | 45 | 23 | 13 | 13 | 9 | 6 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
IBN2 | 100 | 100 | 100 | 99 | 98 | 98 | 99 | 96 | 94 | 90 | 87 | 82 | 88 | 78 | 67 | 71 | 63 | 55 | 49 | 43 | 51 | 43 | 36 | 33 | 25 | 24 | 9 | 13 | 10 | 3 | 8 | 5 | 0 | 4 | 2 | 1 | 0 | 2 | 1 | 0
IBN100 | 100 | 100 | 100 | 99 | 97 | 98 | 99 | 96 | 94 | 89 | 85 | 80 | 86 | 73 | 65 | 67 | 56 | 52 | 46 | 42 | 48 | 38 | 36 | 25 | 20 | 22 | 8 | 12 | 8 | 3 | 8 | 4 | 0 | 4 | 2 | 1 | 0 | 1 | 1 | 0

## Slide 43: Evaluation – 8x8
Chart: 
| 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0 | 110.0 | 120.0 | 130.0 | 140.0 | 150.0 | 160.0 | 170.0 | 180.0 | 190.0 | 200.0 | 210.0 | 220.0 | 230.0 | 240.0 | 250.0 | 260.0 | 270.0 | 280.0 | 290.0 | 300.0 | 310.0 | 320.0 | 330.0 | 340.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 400.0 | 410.0 | 420.0 | 430.0
SB | 100 | 100 | 100 | 100 | 100 | 99 | 100 | 100 | 100 | 98 | 98 | 95 | 96 | 97 | 94 | 95 | 93 | 91 | 88 | 82 | 87 | 84 | 83 | 85 | 78 | 73 | 71 | 76 | 74 | 60 | 63 | 64 | 63 | 58 | 59 | 58 | 52 | 50 | 54 | 46
XLWX | 100 | 100 | 99 | 98 | 91 | 93 | 84 | 85 | 80 | 64 | 58 | 54 | 56 | 45 | 23 | 13 | 13 | 9 | 6 | 3 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
IBN2 | 100 | 100 | 100 | 99 | 98 | 98 | 99 | 96 | 94 | 90 | 87 | 82 | 88 | 78 | 67 | 71 | 63 | 55 | 49 | 43 | 51 | 43 | 36 | 33 | 25 | 24 | 9 | 13 | 10 | 3 | 8 | 5 | 0 | 4 | 2 | 1 | 0 | 2 | 1 | 0
IBN100 | 100 | 100 | 100 | 99 | 97 | 98 | 99 | 96 | 94 | 89 | 85 | 80 | 86 | 73 | 65 | 67 | 56 | 52 | 46 | 42 | 48 | 38 | 36 | 25 | 20 | 22 | 8 | 12 | 8 | 3 | 8 | 4 | 0 | 4 | 2 | 1 | 0 | 1 | 1 | 0
Chart: # flows per flow set
| 80.0 | 90.0 | 100.0 | 110.0 | 120.0 | 130.0 | 140.0 | 150.0 | 160.0 | 170.0 | 180.0 | 190.0 | 200.0 | 210.0 | 220.0 | 230.0 | 240.0 | 250.0 | 260.0 | 270.0 | 280.0 | 290.0 | 300.0 | 310.0 | 320.0 | 330.0 | 340.0 | 350.0 | 360.0 | 370.0 | 380.0 | 390.0 | 400.0 | 410.0 | 420.0 | 430.0 | 440.0 | 450.0 | 460.0 | 470.0 | 480.0 | 490.0 | 500.0 | 510.0 | 520.0
SB | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 98 | 100 | 98 | 100 | 99 | 98 | 96 | 98 | 94 | 95 | 94 | 92 | 96 | 84 | 90 | 91 | 88 | 83 | 91 | 86 | 80 | 81 | 81 | 83 | 74 | 71 | 79 | 71 | 70 | 77 | 65 | 77 | 67
XLWX | 100 | 98 | 98 | 98 | 98 | 96 | 92 | 87 | 83 | 84 | 67 | 62 | 70 | 60 | 54 | 40 | 37 | 37 | 26 | 16 | 20 | 14 | 14 | 10 | 6 | 4 | 1 | 1 | 1 | 0 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
IBN2 | 100 | 100 | 98 | 98 | 100 | 100 | 100 | 97 | 96 | 97 | 86 | 88 | 89 | 84 | 78 | 78 | 63 | 66 | 66 | 51 | 57 | 59 | 43 | 46 | 39 | 32 | 26 | 20 | 19 | 17 | 9 | 3 | 7 | 12 | 2 | 4 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0
IBN100 | 100 | 100 | 98 | 98 | 100 | 100 | 100 | 97 | 96 | 95 | 85 | 86 | 87 | 82 | 78 | 75 | 63 | 61 | 65 | 50 | 56 | 55 | 41 | 44 | 35 | 28 | 21 | 16 | 18 | 16 | 9 | 3 | 7 | 9 | 2 | 4 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 0

## Slide 44: How can we improve this situation?
Mixed Criticality view
Change the wormhole protocol
  Force the world to behave according to the analysis
Can temporal predictability become an emergent property of platform?

## Slide 45: Randomise Behaviour
Allow instruction times to be random
But not necessarily iid, so weakly-independent (e.g. modelled as a Markov chain)
Assumes timing requirements are at the task level (e.g. milliseconds)
Assume task contains a large number of instructions
Can we derive WCET as a simple function of average-case execution time?

## Slide 46: Example with probability of failure 10^-9
1000
10000
100000
1000000
10000000
0.96
0.98
1.00
1.02
1.04
1.06
K
Bayesian (I)
Bayesian (P)
Simple (I)
Simple (P)

## Slide 47: Real Hardware
Can a real platform behave randomly?
Yes if overall behaviour is the sum of many minor effects
In this sense COTS and complex platforms are better!
Consider a 4-core R Pi: contains a number of unmodelled non-deterministic features

## Slide 48: Example

## Slide 49: Conclusions
Modeling the temporal behaviour of modern many-core platforms is hard
Two routes forward:
  Provide managed resource at all levels
  Provide unmanaged resources at all levels
For the former Wormhole routing is an important technology, although changes to the protocol could improve schedulability

## Slide 50: Conclusions
Modeling the temporal behaviour of modern many-core platforms is hard
Two routes forward:
  Provide managed resource at all levels
  Provide unmanaged resources at all levels
For the former Wormhole routing is an important technology, although changes to the protocol could improve schedulability
For the latter a change in mind-set is required!